## Slide 1: RushNet: Practical Traffic Prioritization for Saturated Wireless Sensor Networks
Chieh-Jan Mike Liang†, Kaifei Chen‡, Nissanka Bodhi Priyantha†, Jie Liu†, Feng Zhao†
†Microsoft Research, ‡University of California, Berkeley

## Slide 2: Motivation
How to provide traffic prioritization over saturated radio medium?

## Slide 3: Possible Solutions
Time Division Multiple Access (TDMA)
  Synchronization overhead
  Waste of resource for sporadic and unpredictable events
Frequency Division Multiple Access (FDMA)
  Waste of resource for sporadic and unpredictable events
  Cannot avoid external interference
Carrier Sense Multiple Access
  Does not work for busy networks
Resource Reservation like RSVP
  Setup overhead and delay

## Slide 4: Our Solution: RushNet
a schedule-free and coordination-free 802.15.4 wireless network stack on COTS transceivers that enables packet prioritization
Reserve the highest transmission power for high priority packets
Send high priority packets to preempt on-going normal packets
Cache normal packets by predicting whether they were preempted

## Slide 5: Outline
Motivation and Approach
Naïve Preemption
Preemptive Packet Train
Interference Recovery Caching
Deployment and Evaluation

## Slide 6: Naïve Preemption Experiment
Lower-Power Packets
Higher-Power Packets
100cm
COTS transceivers: Atmel RF231 and TI CC2420
Vary higher power levels
Measure packet reception ratio (PRR) of higher power packets at receiver
Lower Power Transmitter
Higher Power Transmitter
Receiver

## Slide 7: Naïve Preemption Results
Atmel RF231
Lower Power RSS
TI CC2420
Lower Power RSS

## Slide 8: Why Doesn’t Naïve Preemption Work?
802.15.4 Bit Spreading
Atmel RF231 and TI CC2420 have reception state machine

## Slide 9: 802.15.4 Bit Spreading
PNn
PN1
SYNC
Bit Spreading
Low-Power Packets
High-Power Packets
Received Packets
(Corrupted)
pseudo-random noise (PN) sequences
PNn
PN1
SYNC
Bit Spreading
Invalid PN sequence

## Slide 10: 802.15.4 Chip State Machine
Low-Power Packets
High-Power Packets
SYNC
SYNC
Radio Chip
States
SYNC
Listening
Sync
(Lock on the highest power packet)
Reception
(Not preempt-able)
SYNC
SYNC

## Slide 11: Outline
Motivation and Approach
Naïve Preemption
Preemptive Packet Train
Interference Recovery Caching
Deployment and Evaluation

## Slide 12: RushNet Solution
Naïve preemption doesn’t work
RushNet repeats the high priority packet and send back-to-back, which we call a preemptive packet train

## Slide 13: RushNet Preemptive Packet Train
SYNC
SYNC
SYNC
SYNC
Corrupted
Noise
SYNC
Low-Power Packets
A Repeatedly 2-packet
High-Power Packet Train
Received Packets
(1 High Power Packet)
Repeated packet

## Slide 14: Preemptive Packet Train Experiment Setup
Same setup as naïve approach EXCEPT
  Only use TI CC2420
  Vary high power packet train length from 2 to 7
Lower-Power Packets
Higher-Power Packets
100cm
Lower Power Transmitter
Higher Power Transmitter
Receiver

## Slide 15: Preemptive Packet Train Performance

## Slide 16: What Happens to Normal Packets
Higher power packet train can preempt normal packets
What happens to these normal packets?

## Slide 17: Outline
Motivation and Approach
Naïve Preemption
Preemptive Packet Train
Interference Recovery Caching
Deployment and Evaluation

## Slide 18: Interference Recovery Caching
Memory size is limited
RushNet predicts most possibly destroyed normal packets using tail channel signal strength
Lower-Power Packets
Higher-Power Packets
Memory
Lower Power Transmitter
Higher Power Transmitter
Receiver

## Slide 19: Predict Packet Loss After Transmission
Category 1
Category 3
Channel SS
Category 2
Channel SS
Category 3
Channel SS
Category 1: Very likely to be lost
Category 2: Less likely to be lost
Category 3: Unlikely to be lost
Channel SS
Channel SS
> threshold
CSS

## Slide 20: Packet Caching Experiment Setup
Lower-Power Packets
Higher-Power Packets
50cm
Lower Power Transmitter
Higher Power Transmitter
Receiver
1700 Packets
1700 tail Channel Signal Strengths
Reception Prediction Algorithm
Compare output with Ground Truth at receivers

## Slide 21: Packet Reception Prediction
Correct Prediction: ~90%
Predict All Lost
Predict All Received

## Slide 22: Outline
Motivation and Approach
Naïve Preemption
Preemptive Packet Train
Interference Recovery Caching
Deployment and Evaluation

## Slide 23: Office Deployment
41 TelosB motes (TI CC2420)
Run our WRAP protocol in SenSys’09 paper1, which uses a tree topology and token-based multiple access
Each mote generates one normal packet per 15 seconds
We randomly send 100 higher power packets with train length 4 on a 5-hop branch over 10 minutes, and measure their latencies and PRRs
1. Liang et al. RACNet: a high-fidelity data center sensing network. SenSys’09.

## Slide 24: High Power Packet Latency and PRR

## Slide 25: Conclusions
RushNet enables practical packet prioritization on 802.15.4 wireless sensor network
It uses a back-to-back train of preemptive repeated high power packet to preempt normal packet, we can achieve 90% PRR with 4-packet train
It uses tail channel signal strength sampling to predict packet collision for better caching efficiency, we can achieve ~90% prediction accuracy

## Slide 26
Thank you!